## Slide 1
AdaCFAR-1D
Deep Adaptive Detection for Heterogeneous Radar Clutter
Daniel Attali & Sapir Bashan Deep Learning Course | 26/06/2026

## Slide 2
Radar Detection Problem
AdaCFAR-1D | Deep Learning Course | 2
Detection is the first hard decision in the radar chain
Missed detections reduce target observability
False alarms overload downstream tracking and association
Two-way propagation delay

## Slide 3
Classical Solution: CA-CFAR
AdaCFAR-1D | Deep Learning Course | 3
Local noise estimate
Adaptive threshold
Works well in homogeneous environments

## Slide 4
The Problem: Target Masking
AdaCFAR-1D | Deep Learning Course | 4
Training cells include high-power clutter
Estimated noise floor becomes biased upward
Threshold rises and masks nearby targets
Target can satisfy

## Slide 5
Key Observation: CFAR is a Fixed Convolution
AdaCFAR-1D | Deep Learning Course | 5
CFAR is not unrelated to deep learning — it is already convolutional
The difference: CFAR weights are hand-designed and fixed
Conv1D weights can be learned for the target clutter regime

## Slide 6
Research Question
AdaCFAR-1D | Deep Learning Course | 6
Can a learned Conv1D detector outperform fixed CA-CFAR in heterogeneous clutter?
CA-CFAR Fixed detector Manual parameters Analytical assumptions
AdaCFAR-1D Learned detector Task-specific parameters Trained on simulated radar profiles

## Slide 7
Dataset Generation
AdaCFAR-1D | Deep Learning Course | 7
Targets
Radar Eq.
Beamforming
Pulse Compression
Envelope
NCI
1D Profile
Clutter + Mask
Item | Value
Training profiles | 25,000
Validation profiles | 1,000
Range gates | 1024
Targets/profile | 0–4
SNR range | 15–30 dB
Stress clutter multiplier | 5.0

## Slide 8
Example Training Sample
AdaCFAR-1D | Deep Learning Course | 8
Labels are generated from the clean processed target response
The target is not a single bin: it occupies the pulse-compressed response

## Slide 9
AdaCFAR Architecture
AdaCFAR-1D | Deep Learning Course | 9
Wide first kernel captures pulse morphology
Dilated convolutions capture long-range clutter context
Skip connection preserves local target features
40k Parameters (very small for RT inference)

## Slide 10
Training Performance
AdaCFAR-1D | Deep Learning Course | 10
We had to find a suitable loss function:

## Slide 11
Detection Probability: CA-CFAR vs AdaCFAR
AdaCFAR-1D | Deep Learning Course | 11
SNR | CA-CFAR | AdaCFAR V4 | Improvement
30 dB | 78.4% | 88.5% | +10.1 pts
25 dB | 68.8% | 82.4% | +13.6 pts
20 dB | 55.6% | 71.7% | +16.1 pts
15 dB | 41.3% | 58.9% | +17.6 pts
AdaCFAR improves at every tested SNR
The gain grows as the scenario becomes harder

## Slide 12
False Alarm Performance
AdaCFAR-1D | Deep Learning Course | 12
SNR | CA-CFAR FA | AdaCFAR V4 FA
30 dB | 285 | 0
25 dB | 287 | 7
20 dB | 291 | 3
15 dB | 278 | 7
False alarms are counted as connected predicted components
The final model improves detection without flooding the tracker

## Slide 13
Qualitative Comparison: V4 vs CA-CFAR
AdaCFAR-1D | Deep Learning Course | 13
Chart: 
| 20 dB Pd | 15 dB Pd | 20 dB FA | 15 dB FA
CA-CFAR | 55.6 | 41.3 | 291 | 278
AdaCFAR V4 | 71.7 | 58.9 | 3 | 7
The chart mixes Pd (%) and FA counts for visual contrast only
Use actual profile figure for final qualitative evidence

## Slide 14
Conclusions
AdaCFAR-1D | Deep Learning Course | 14
CA-CFAR can be interpreted as a fixed convolutional detector
AdaCFAR-1D learns a task-specific Conv1D detection rule
The final model improves detection probability while suppressing false alarms
This is a proof of concept, not a general CFAR replacement
Manual detector → learned adaptive detector

## Slide 15
AdaCFAR-1D | Deep Learning Course | 15
Questions?
Daniel Attali & Sapir Bashan